## Slide 1: Green Production of Terephthalic Acid for the Synthesis of PETE
Team 3: Timothy Chen, Qingyuan Liu, Tom Sikorski, Yiqi Wang
May 12, 2016

## Slide 2: Outline
PETE Production
Green Routes
Isobutanol to P-xylene Process
CHEMCAD Simulation
Economic Analysis
Environmental, Health, and Safety Concerns
Sustainability and Concluding Remarks

## Slide 3: Polyethylene Terephthalate (PETE)
One of the most common types of polymers
Global PETE production in 2015 was estimated to reach 24.39 million tons†
Lightweight, impact resistance, and chemical resistance make it ideal for food packaging, plastic bottles, and textiles
† Merchant Research & Consulting, Ltd. http://mcgroup.co.uk/news/20140117/global-pet-supply-exceed-2439-mln-tonnes-2015.html

## Slide 4: PETE Production
Typically produced with terephthalic acid (TPA) and ethylene glycol (EG)
Undergo condensation reactions in esterification vessels forming BHET
Followed by polymerization in reactors to form PETE
†U.S. Environmental Protection Agency, “Compilation of Air Pollutant Emission Factors,” Publication AP-42, https://www3.epa.gov/ttnchie1/ap42/ch06/final/c06s06-2.pdf, EPA, Office of Air Quality Planning and Standards, Research Triangle Park, NC (Jan. 1995).
Notes: bio-hydroxyethyl terephthalate (BHET)

## Slide 5: Green Routes Overview
BIOMASS
PX
TPA
P-cymene
isoprene and acrylic acid
Furfural
Limonene
4-methylcyclohex-3-enecarboxylic acid
Maleic anhydride
Fermentation
Sugar Cane
Sugar
Isobutanol
Isobutylene
HMF
Ethanol
DMF
Ethylene
Fermentation
Enzyme
†Based on figure from Pang et.al. Synthesis of ethylene glycol and terephthalic from biomass for producing PET. Green Chem. 2016,18, 342.

## Slide 6: Green Routes: Isobutanol and HMF Routes
HMF pathway (CCEI) †
Isobutanol pathway (GEVO)†
†Reaction pathways taken from Pang et.al. Synthesis of ethylene glycol and terephthalic from biomass for producing PET. Green Chem. 2016,18, 342.
†† Z. Lin; V. Nikolakis; M. Ieraptetritou, Ind. Eng. Chem. Res., 2014, 53, 10688-10699.
Estimated p-xylene cost of $3,962/mt††
Large capital cost from expensive Cu-Ru/C catalyst
Catalyst replacement is also majority of operating cost
Large solvent usage (THF, n-heptane)
Estimated p-xylene cost of $3,481/mt††
Majority of operating cost from raw material (starch) price(46%)
Valuable side products (o-xylene, benzene,etc)
Petroleum based p-xylene is at $1630/mt

## Slide 7: Isobutanol and HMF Routes: Promise of Isobutanol
Heavy research into its production already underway- Isobutanol has similar octane rating and energy density as gasoline.†
Main challenge is effective bio-based production of isobutanol
World’s first renewable HMF facility (2013) – 20 tons/year.††
GEVO isobutanol plant projected to produce 400 million gallons/year (~1.2 million metric tons/year).†††
World oil production: barrels/year (4.7 billion metric tons/year)††††
† Advanced Motor Fuels. http://www.iea-amf.org/content/fuel_information/butanol/properties
†† First Industrial Production For Renewable 5-HMF
https://chemicalparks.eu/news/2014-2-3-first-industrial-production-for-renewable-5-hmf
††† Second-Generation Biofuel: Isobutanol Producing Biocatalyst
https://www.epa.gov/sites/production/files/2015-06/documents/gevo010711.pdf
†††† International Energy Statistics 2014 https://www.eia.gov/cfapps/ipdbproject/IEDIndex3.cfm?tid=5&pid=53&aid=1

## Slide 8: Isobutanol to P-xylene Process
Feed rate of 150 million kg/year (17123 kg/hr) of isobutanol
  Chosen to be on same order of magnitude as 5% of current NA PETE production
  Use 30% mole fraction isobutanol
    26839 kg/hr flow rate of isobutanol-water mixture
Shell and tube heat exchangers with floating tube sheet heads
Most equipment made from carbon steel
  Copper or titanium used when hydrogen present
  Stainless steel for fired heater
Pressure drop in system dealt with by oversizing pumps
  System insensitive in general to local pressure increases
  Over pressurize system to account for pressure drop
Produces 99.5 % and 99.7 % purity p-xylene

## Slide 9: PFD Overview

## Slide 10: PFD Part 1 - Dehydration
Raise pressure to 10 bar
Product heat exchangers
Decanter
Fully condense process stream (30 °C)
Raise pressure to 15 bar
Dehydration reactor (325 °C) for production of isobutene

## Slide 11: PFD Part 2 – Oligomerization and Dehydrocyclization

## Slide 12: PFD Part 2 – Oligomerization and Dehydrocyclization
Isobutene
Oligomerization Reactive Distillation to form DIB
Vaporize stream to use in gas turbine
Heat stream to 500 °C for dehydrocylization reactor
Dehydrocyclization reactor for formation of PX
Product heat exchanger

## Slide 13: PFD Part 3 – Separations

## Slide 14: PFD Part 3 – Separations
PX and hydrocarbons
Flash off virtually all of methane and hydrogen
Distillation to remove C4
Distillation to remove DIB
Distillation to remove TIB from PX
Distillation to remove TIB from PX

## Slide 15: Simulation Overview
Single simulation to detect process wide effects of changes
Pieces result in recycle streams not matching in terms of mass balances
Sections ran individually for convergence before including recycle streams, then combined until entire simulation converged
Multiple thermodynamic models used, local models applied where needed; selected based on Don’t Gamble with Physical Properties for Simulation†
†Carlson, E. Don’t Gamble with Physical Properties for Simulation. Chemical Engineering Progress. 1996.
Notes: Best practice to confirm VLE data in simulation with experimental data, little to no resources on the VLE data for particular components (i.e. p-xylene and DIB VLE, p-xylene and TIB VLE, isobutene and DIB VLE, isobutene and p-xylene VLE, etc.).
Most of process run at 10 bar and was highly non-ideal, global UNIFAC/LATE model chosen.
Reactive distillation column run at 15 bar, and heuristics said PSRK outperform UNIFAC at higher pressures, so PSRK/LATE chosen as a local model
UNIFAC unable to accurately reproduce solubility of isobutene and water even with water/hydrocarbon selected as immiscible and they are known to be nearly insoluble in water so UNIFAC model was inappropriate for liquid-liquid separator. However, UNIFAC LLE is extension of UNIFAC and dedicated to modeling liquid liquid equilibrium. This model had water and isobutene phases correctly partitioning in separator and recommended model for liquid-liquid systems.
Rest of the simulation was run using the global thermodynamic model.

## Slide 16: Simulation Overview

## Slide 17: First Reaction

## Slide 18: First Reaction
Done with two reactors as kinetics for butene side product could not be found
Paper studying kinetics of isobutanol dehydration†
  Conversion of isobutanol was 99% & Selectivity was 95%
  Our conversion was 97% with 95% selectivity
Major side products linear butenes, collectively represented by trans-2-butene
† Dehydration of isobutanol to isobutene in a slurry reactor (Technical Report) | SciTech Connect. http://www.osti.gov/scitech/biblio/171265

## Slide 19: Second Reaction

## Slide 20: Second Reaction
SCDS column with reactive distillation option used with di-isobutylenes collectively represented by 1-di-isobutylene
Reality, reactions involving formation of tert-butyl alcohol from water affecting rate of oligomerization and selectivity
  IB + IB  DIB
  DIB + IB  TIB
  TIB + IB  TEB
  IB + H2O  TBA
  TBA  IB + H2O
Couldn’t converge for complex kinetic equations, only two reactions specified
Notes: Formation of tetramers assumed negligible as described by paper studying this oligomerization reaction

## Slide 21: Third Reaction

## Slide 22: Third Reaction
Direct kinetics of dehydrocyclization for di-isobutylene (2,4,4-Trimethyl-1-Pentene) to p-xylene not available
Similar kinetics for 2,4,4-Trimethyl-Pentane
Rate expression simulated in kinetic reactor using user defined VBA expression

## Slide 23: Third Reaction
Harsh conditions caused many side products due to cracking, infeasible to simulate all kinetics
14 parallel stoichiometric reactors used to form side products before entering main reactor
Streams from all reactors combined into kinetic reactor with rate law
After optimizing and sizing kinetic reactor replaced with stoichiometric
Notes: Cracking reaction : where high-carbon-number molecules cracks into low-carbon-number molecules
divider allocates feed portion to each reaction as if in a single reactor, allocated streams then enter stoichiometric reactors set with 100% conversion
The conversion of the products pre-determined based on ratio of streams split.
Kinetic reactor did not behave well in large scale simulation

## Slide 24: Recycle & Side Product Separation

## Slide 25: Recycle & Side Product Separation
Component separator used after flash to remove H2 & CH4 as there is virtually none left after flash
ChemCAD attempts to lower temp of stream below 0°C to condense this small amount of H2 & CH4 causing convergence problems and greatly skewing duties

## Slide 26: Optimization
Sensitivity studies ran on equipment comparing variables usually to amount of a component in product stream
  Amount of desired product out of reactor
  How much of component left after separation
Values chosen to get best conversion or separation before there was greatly diminished returns
Notes: Value chosen that would cost less when plot started to level off.

## Slide 27: Economic Analysis: Capital Costs
Equipment Sizing + CAPCOST
2015 CEPCI of 537
Grass Roots
  15 % for contingency costs
  3 % for fees
Land cost of $450,000
Location: North American Midwest
Grassland biome†
† What is a grassland biome? Web. (accessed May 8, 2016). ask.com

## Slide 28: Equipment Sizing: Heat Exchanger
Shell and tube heat exchanger
Parameters required to be sized:
  Area of heat exchanger
http://www.indothermindustries.com/product%209.html

## Slide 29: Equipment Sizing: Flash Tank
Parameters required for sizing:
  Density of vapor stream
  Density of liquid stream
  Mass flow rate of vapor stream
  Mass flow rate of liquid stream

## Slide 30: Equipment Sizing: Decanter
Parameters required for sizing:
  Density of heavy phase stream
  Density of light phase stream
  Volumetric flow rate of heavy phase stream
  Kinetic viscosity of mixed stream

## Slide 31: Equipment Sizing: Distillation Column
Parameters required for sizing:
  Density of heavy phase stream
  Density of light phase stream
  Mass flow rate of vapor stream
  Mass flow rate of liquid stream
  Kinetic viscosity of entering stream
  Number of trays

## Slide 32: Equipment Sizing: Reactors
R-101: multi-tubular packed bed reactor
  Similar to a shell and tube heat exchanger but has catalyst
  Heat duty of the reactor (6169 MJ/hr) → minimum heat exchanging area
  Heat exchanging area
    Assumption: heat transfer coefficient: 300W/m2K; heating agent: in at 360 °C, out at 330 °C
  Estimate number of tubes for given radius and length
    Determine number of tubes for optimized reactor volume then determine surface area of those tubes
R-102: reactive distillation reactor
  Sized like distillation column with additional cost of catalyst

## Slide 33: Equipment Sizing: Reactor 103
Fixed Bed Column
  Mass of catalyst using → Volume of catalyst
  Assume cylindrical shaped reactor
  Total pressure drop of the reactor is limited to 10% of inlet pressure
  Pressure drop per length calculated (Ergun Equation)
  Pressure drop → Length of the reactor
  Length of the reactor & Radius → volume of the reactor
  Compare volume of the reactor to volume of the catalyst

## Slide 34: Economic Analysis: Cost of Manufacturing
Operator cost
    P = 0, Nnp = 16, NOL = 3.16
  4 active operators per shift
    18 operators on payroll
    Illinois annual median wage for operator is $55,690
Utility cost – used default costs in CAPCOST
  Heater utility cost was neglected due to sufficient fuel being provided from hydrocarbons produced in process (1.03 x 105 MJ/h)

## Slide 35: Economic Analysis: Cost of Manufacturing
Chemical | 2006 Price ($/kg) | Projected 2016 Price ($/kg) | Source
Isobutanol | - | 1.15-$1.48 | GEVO
Terepthalic Acid | 0.925 | 1.066 | ICIS
P-xylene | 1.43 | 1.53 | ICIS
Ni-Al2O3 (1% by mass Ni loading) | - | 4272 | RiogenInc
γ-alumina | - | 15.60 | AdvancedMaterials
Platinum on Carbon | - | 9890 | RiogenInc
Isobutylene | 0.70 | 0.752 | ICIS
Di-isobutylene | - | 1.25 | Zauba
Chemical Pricing from ICIS, GEVO, etc
  Catalyst prices used were laboratory prices

## Slide 36: Economic Analysis:Profitability
Additional Assumptions:
  10 % discount rate
  18% hurdle rate
  7 year MACRS depreciation
  8500 hours of operation a year
  15 year project lifetime (not including construction)
  No salvage
  Assume half of catalyst replaced each year
Two scenarios evaluated: selling PX or TPA as a product

## Slide 37: Economic Analysis: Profitability
Selling PX as Product
  NPV of -$52.3 million
  Undefined payback period
Increase at end is CAPCOST factoring in cost of land and capital costs

## Slide 38: Economic Analysis: Profitability
Selling TPA as product
Used Capital cost and COM without PX from Team 5 ($61.7 and $89 million respectively)
  Scaled their costs to the ratio of their PX feed rate and our PX production rate (FCI and COM adjusted to $40 and $58.3 million respectively
  NPV of -$524.3 million
  Undefined payback period

## Slide 39: Profit Conditions
As is, process not generating profit
Two scenarios investigated, increase in price of p-xylene and the decrease in price of impure isobutanol used
Prices were changed until the projected value on the cash flow diagram evened out to 0 at end of 17 years
  Above $1.77 per kg of p-xylene (was $1.53)
  Below $0.37 per kg of isobutanol (was $0.44)
Notes: Add cash flow diagrams

## Slide 40: Environmental, Health, and Safety Concerns
All reagents are flammable
  Need to be stored in appropriate, cool, well-ventilated area
Chemicals not corrosive
Some chemicals (e.g. p-xylene) are hazardous to aquatic environment
Waste water must be disposed of appropriately
  Required compliance with federal, state, and local environmental regulations

## Slide 41: Piping and Instrumental Diagram R-101
R – Reactor
P – Pressure
T – Temperature
V – Valve
F – Flow
9Bar 325C 26839kg/h
9Bar 325C 26839kg/h
30% isobutanol
70% water
0.12% isobutanol 76.9% water 21.8% 2-Methylpropene 1.15% trans-2-butene
Thermal oil
Thermal oil
Double Block & Bleed Valve
Double Block & Bleed Valve
RV-101

## Slide 42: Sustainability
Environmentally friendly as raw material generated from bio sources, greatly reduces impact of TPA process
Image better received by public as being green seen as responsible and is becoming more popular
Prepared for petroleum raw material running out or politically difficult to obtain
Becomes profitable as technology to reduce raw material price develops or as current price of oil increases
Differentiates commodity product by being green

## Slide 43: Concluding Remarks***

## Slide 44
Supplementary Slides

## Slide 45
 | Cost ($/GJ)
Common Utilities | 
Electricity (110V - 440V) | 16.8
Cooling Water (30°C to 45°C) | 0.354
Refrigerated Water (15°C to 25°C) | 4.43
Steam from Boilers | 
Low Pressure (5 barg, 160°C) | 13.28
Medium Pressure (10 barg, 184°C) | 14.19
High Pressure (45 barg, 260°C) | 17.7
Fuels | 
Fuel Oil (no. 2) | 14.2
Natural Gas | 11.1
Coal (FOB mine mouth) | 1.72
CAPCOST Default Utility Pricing
 | Cost ($/GJ)
Common Utilities | 
Thermal Systems | 
Moderately High (up to 330°C) | 12.33
High (up to 400°C) | 13
Very High (up to 600°C) | 13.88
Refrigeration | 
Moderately Low (5°C) | 4.43
Low (-20°C) | 7.89
Very low (-50°C) | 13.11
 | Cost ($/tonne)
Waste Disposal (solid and liquid) | 
Non-Hazardous | 36
Hazardous | 200

## Slide 46: Heat obtained from stream sent to H-101
Chemicals | Heat of Combustion (MJ/kg) | Flow Rate (kg/h)
Isobutanol | 33 | 4.85
P-xylene | 40.8 | 21.7
Toluene | 41 | 4.02
Methane | 50 | 7.35
Propene | 48.9 | 27.2
2-Methyl-1-butene | 47.5 | 4.66
2-Methy-1-pentene | 44.8 | 2.04
1-heptene | 47.4 | 35.2
2-Methyl propene | 48.1 | 535
Trans-2-butene | 45.1 | 149.4
1-Diisobutylene | 44 | 113.4
Hydrogen | 142 | 423.2
2,3-dimethyl-1-hexene | 45 *estimated | 8.28
Heat≈1.03*105MJ/h

## Slide 47: Sample Optimization: R-101 Pressure
First Reactor plots of volume, temperature, and pressure

## Slide 48: Sample Optimization: T-101 V/B Ratio
First distillation column plots of the number of stages, the feed stage location, the reflux ratio, and the V/B ratio compared to the isobutylene and di-isobutylene in the bottoms

## Slide 49: Supplementary: Flash tank sizing
Flash Tank
(Souders-Brown Equation)
Rule of thumb: Height/Diameter 3~5

## Slide 50: Supplementary: Decanter Sizing
Decanter

## Slide 51: Supplementary: Equipment Sizing
Distillation Column
Rule of Thumb:
  = 0.8
  range from 0.1 to 0.2
  Height of vapor engagement: larger than 4 ft
  Height of reboiler return: larger than 3 ft
  Height of skirt: 15 ft
  Liquid holding up time: 5 min

## Slide 52: Piping and Instrumental Diagram T-103
0.44% O-xylene
99.1% P-xylene
0.44% Triisobutylene
0.29% O-xylene
99.7% P-xylene
0.93% O-xylene
97.14% P-xylene
1.9% Triisobutylene
2.75Bar 180C 7400kg/h
2.75Bar 180.1C 5680.8kg/h
2.75Bar 180.7C 1719.1kg/h